## Slide 1: CMSC 125: Operating Systems
Instructor: Joseph Anthony C. Hermocilla
Email: jchermocilla@up.edu.ph
Web: https://jachermocilla.org

## Slide 2: Resources
Book: https://pages.cs.wisc.edu/~remzi/OSTEP/
Slides Template:
https://pages.cs.wisc.edu/~remzi/OSTEP/Educators-Slides/Youjip/

## Slide 3: Acknowledgement
This lecture slide set was initially developed for Operating System course in Computer Science Dept. at Hanyang University. This lecture slide set is for OSTEP book written by Remzi and Andrea at University of Wisconsin.

## Slide 4
16. Segmentation
Operating System: Three Easy Pieces

## Slide 5: Inefficiency of the Base and Bounds Registers Approach
Big chunk of “free” space
“free” space takes up physical memory.
Hard to run when an address space does not fit into physical memory
(free)
14KB
Program Code
16KB
0KB
2KB
4KB
Heap
Stack
6KB
15KB
5KB
3KB
1KB

## Slide 6: Segmentation: Generalized Base and Bounds
Motivation: Why not have a base and bounds registers for each logical section in a process’ address space?
A segment is just a contiguous portion of the address space of a particular length
  Logically-different segment: code, stack, heap
Each segment can be placed in different part of physical memory
  Base and Bounds registers exist per segment

## Slide 7: Placing Segments In Physical Memory
0KB
16KB
32KB
48KB
64KB
Code
Physical Memory
(not in use)
(not in use)
Heap
Stack
Operating System
(not in use)
Segment Base Size
Code 32K 2K
Heap 34K 2K
Stack 28K 2K

## Slide 8: Segmentation: Address Translation Example
Assume a reference to virtual address 100 (in code section)
  Since code section starts at 0 in address space, offset is 100
Segment Base Size
Code 32K 2K
0KB
2KB
Program Code
4KB
16KB
32KB
100
instruction
Heap
Code
(not in use)
(not in use)
34KB
is the desired physical address

## Slide 9: Segmentation: Address Translation Example (Cont.)
Assume a reference to virtual address 4200 (in head section)
  The heap section starts at virtual address 4096(4KB) in address space, offset=4200-4096=104
Segment Base Size
Heap 34K 2K
32KB
Heap
Code
(not in use)
(not in use)
34KB
is the desired physical address
6KB
Heap
4KB
Address Space
Physical Memory
4200
data
36KB
is not the correct physical address.

## Slide 10: Segmentation Fault or Segmentation Violation
If an illegal address, such as 7KB, which is beyond the end of heap is referenced, the OS generates segmentation fault.
  The hardware detects that address is out of bounds.
6KB
Heap
4KB
(not in use)
Address Space
7KB
8KB

## Slide 11: Referring to a Segment(Cont.)
Given just a virtual address, how does the hardware determine the segment and offset?
Explicit approach
  Chop up the address space into segments based on the top few bits of virtual address
  Example: virtual address: 4200 (01000001101000)
0
13
1
12
2
11
3
10
4
9
8
7
6
5
Segment
Offset
0
13
1
12
2
11
3
10
4
9
8
7
6
5
Segment
Offset
0
0
0
1
0
0
1
0
0
0
0
0
1
1
Segment bits
Code 00
Heap 01
Stack 10
- 11

## Slide 12: Referring to a Segment(Cont.)
    SEG_MASK = 0x3000(11000000000000)
    SEG_SHIFT = 12
    OFFSET_MASK = 0xFFF (00111111111111)
  Disadvantages of explicit approach using top 2 bits
    If only 3 sections, then 2 bits to store segment is wasteful
    Limits a segment size, ex. max segment size is 4KB
Implicit approach – determines segment based on how the virtual address was generated, ex. if from program counter, then code segment
1 // get top 2 bits of 14-bit VA
2 Segment = (VirtualAddress & SEG_MASK) >> SEG_SHIFT
3 // now get offset
4 Offset = VirtualAddress & OFFSET_MASK
5 if (Offset >= Bounds[Segment])
6 RaiseException(PROTECTION_FAULT)
7 else
8 PhysAddr = Base[Segment] + Offset
9 Register = AccessMemory(PhysAddr)

## Slide 13: Referring to Stack Segment
Stack grows backward!
Extra hardware support is needed
  The hardware checks which way the segment grows.
  1: positive direction, 0: negative direction
Segment Base Size Grows Positive?
Code 32K 2K 1
Heap 34K 2K 1
Stack 28K 2K 0
Stack
(not in use)
(not in use)
28KB
26KB
Physical Memory
Segment Register(with Negative-Growth Support)

## Slide 14: Referring to Stack Segment(Cont.)
Example: reference to virtual address 15KB = 11 1100 0000 0000 = 0x3C00
Segment=0x3(3), Offset=0xC00 (3KB)
Negative Offset = Offset - Max Segment Size = 3KB - 4KB = -1KB
Physical Address = Negative Offset + Stack Base
Physical Address = -1KB + 28KB = 27KB

## Slide 15: Support for Sharing
Segment can be shared between address space
  Code sharing is still in use in systems today
  by using extra hardware support
Extra hardware support is needed: Protection Bits
  A few more bits per segment to indicate permissions of read, write and execute
Segment Base Size Grows Positive? Protection
Code 32K 2K 1 Read-Execute
Heap 34K 2K 1 Read-Write
Stack 28K 2K 0 Read-Write
Segment Register Values(with Protection)

## Slide 16: Fine-Grained and Coarse-Grained Segmentation
Coarse-Grained means segmentation in a small number
  e.g., code, heap, stack
Fine-Grained segmentation allows more flexibility for address space in some early system
  To support many segments, hardware support with a segment table is required

## Slide 17: OS Support for Segmentation
What should the OS do during context switch?
What should the OS do when a segment grows?
How should the free space in memory be managed?
  There are variable segment sizes

## Slide 18: OS Support for Segmentation: Managing Fragmentation
External Fragmentation: little holes of free space in physical memory that make it difficulty to allocate new segments
  There is 24KB free, but not in one contiguous segment
  The OS cannot satisfy a 20KB request
Compaction: rearranging the existing segments in physical memory
  Compaction is costly
    Stop running process.
    Copy data to somewhere
    Change segment register value
Better to use a free-list management algorithm
  Keep large extends of memory available for allocation
  Approaches: best-fit, worst-fit, buddy-algorithm

## Slide 19: Memory Compaction
0KB
16KB
32KB
48KB
64KB
Not compacted
Operating System
8KB
24KB
40KB
56KB
Allocated
(not in use)
0KB
16KB
32KB
48KB
64KB
Operating System
8KB
24KB
40KB
56KB
(not in use)
(not in use)
Allocated
(not in use)
Allocated
Allocated
Compacted