## Slide 1: CMSC 125: Operating Systems
Instructor: Joseph Anthony C. Hermocilla
Email: jchermocilla@up.edu.ph
Web: https://jachermocilla.org

## Slide 2: Resources
Book: https://pages.cs.wisc.edu/~remzi/OSTEP/
Slides Template:
https://pages.cs.wisc.edu/~remzi/OSTEP/Educators-Slides/Youjip/

## Slide 3: Acknowledgement
This lecture slide set was initially developed for Operating System course in Computer Science Dept. at Hanyang University. This lecture slide set is for OSTEP book written by Remzi and Andrea at University of Wisconsin.

## Slide 4
20. Paging: Smaller Tables
Operating System: Three Easy Pieces

## Slide 5: Paging: Linear Tables
We usually have one page table for every process in the system.
  Assume that 32-bit address space with 4KB pages and 4-byte page-table entry.
Page table size =
Page 0
Page 1
Page 2
Physical Memory
Page n
…
entry
…
entry
entry
entry
Page Table of
Process A
4B
4KB
Page table are too big and thus consume too much memory.
Notes: 여백 감소 페이지 사이의 간격을 없애기.

## Slide 6: Paging: Smaller Tables
Page table are too big and thus consume too much memory.
  Assume that 32-bit address space with 16KB pages and 4-byte page-table entry.
Page 0
Page 1
Page 2
Physical Memory
Page n
…
entry
…
entry
entry
entry
Page Table of
Process A
4B
16KB
per page table
Big pages lead to internal fragmentation.
Notes: 여백 감소 페이지 사이의 간격을 없애기.

## Slide 7: Problem
Single page table for the entries address space of process.
 | 0
 | 1
 | 2
 | 3
 | 4
 | 5
 | 6
 | 7
 | 8
 | 9
 | 10
 | 11
 | 12
 | 13
 | 14
code
heap
stack
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
Allocate
Virtual Address
Space
Physical Memory
A 16KB Address Space with 1KB Pages
PFN | valid | prot | present | dirty
10 | 1 | r-x | 1 | 0
- | 0 | - | - | -
- | 0 | - | - | -
- | 0 | - | - | -
15 | 1 | rw- | 1 | 1
… | … | … | … | …
- | 0 | - | - | -
3 | 1 | rw- | 1 | 1
23 | 1 | rw- | 1 | 1
A Page Table For 16KB Address Space

## Slide 8: Problem
Most of the page table is unused, full of invalid entries.
 | 0
 | 1
 | 2
 | 3
 | 4
 | 5
 | 6
 | 7
 | 8
 | 9
 | 10
 | 11
 | 12
 | 13
 | 14
code
heap
stack
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
Allocate
Virtual Address
Space
Physical Memory
A 16KB Address Space with 1KB Pages
PFN | valid | prot | present | dirty
10 | 1 | r-x | 1 | 0
- | 0 | - | - | -
- | 0 | - | - | -
- | 0 | - | - | -
15 | 1 | rw- | 1 | 1
… | … | … | … | …
- | 0 | - | - | -
3 | 1 | rw- | 1 | 1
23 | 1 | rw- | 1 | 1
A Page Table For 16KB Address Space

## Slide 9: Hybrid Approach: Paging and Segments
In order to reduce the memory overhead of page tables.
  Using base not to point to the segment itself but rather to hold the physical address of the page table of that segment.
  The bounds register is used to indicate the end of the page table.

## Slide 10: Simple Example of Hybrid Approach
Each process has three page tables associated with it.
  When process is running, the base register for each of these segments contains the physical address of a linear page table for that segment.
Seg
VPN
Offset
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Seg value | Content
00 | unused segment
01 | code
10 | heap
11 | stack
32-bit Virtual address space with 4KB pages

## Slide 11: TLB miss on Hybrid Approach
The hardware get to physical address from page table.
  The hardware uses the segment bits(SN) to determine which base and bounds pair to use.
  The hardware then takes the physical address therein and combines it with the VPN as follows to form the address of the page table entry(PTE) .
01: SN = (VirtualAddress & SEG_MASK) >> SN_SHIFT
02: VPN = (VirtualAddress & VPN_MASK) >> VPN_SHIFT
03: AddressOfPTE = Base[SN] + (VPN * sizeof(PTE))

## Slide 12: Problem of Hybrid Approach
Hybrid Approach is not without problems.
  If we have a large but sparsely-used heap, we can still end up with a lot of page table waste.
  Causing external fragmentation to arise again.

## Slide 13: Multi-level Page Tables
Turns the linear page table into something like a tree.
  Chop up the page table into page-sized units.
  If an entire page of page-table entries is invalid, don’t allocate that page of the page table at all.
  To track whether a page of the page table is valid, use a new structure, called page directory.

## Slide 14: Multi-level Page Tables: Page directory
201
PBTR
Linear Page Table
Multi-level Page Table
valid
prot
PFN
1 | rx | 12
1 | rx | 13
0 | - | -
1 | rw | 100
0 | - | -
0 | - | -
0 | - | -
0 | - | -
0 | - | -
0 | - | -
1 | rw | 86
1 | rw | 15
PFN201
PFN202
PFN203
1 | 201
0 | -
0 | -
1 | 203
The Page Directory
PFN200
valid
PFN
1 | rx | 12
1 | rx | 13
0 | - | -
1 | rw | 100
PFN201
valid
prot
PFN
[Page 1 of PT:Not Allocated]
[Page 2 of PT: Not Allocated]
0 | - | -
0 | - | -
1 | rw | 86
1 | rw | 15
PFN204
200
PBTR
Linear (Left) And Multi-Level (Right) Page Tables

## Slide 15: Multi-level Page Tables: Page directory entries
The page directory contains one entry per page of the page table.
  It consists of a number of page directory entries(PDE).
PDE has a valid bit and page frame number(PFN).

## Slide 16: Multi-level Page Tables: Advantage & Disadvantage
Advantage
  Only allocates page-table space in proportion to the amount of address space you are using.
  The OS can grab the next free page when it needs to allocate or grow a page table.
Disadvantage
  Multi-level table is a small example of a time-space trade-off.
  Complexity.

## Slide 17: Multi-level Page Table: Level of indirection
A multi-level structure can adjust level of indirection through use of the page directory.
  Indirection place page-table pages wherever we would like in physical memory.

## Slide 18: A Detailed Multi-Level Example
To understand the idea behind multi-level page tables better, let’s do an example.
Flag | Detail
Address space | 16 KB
Page size | 64 byte
Virtual address | 14 bit
VPN | 8 bit
Offset | 6 bit
Page table entry | 
Flag | Detail
Address space | 16 KB
Page size | 64 byte
Virtual address | 14 bit
VPN | 8 bit
Offset | 6 bit
Page table entry | 
code
code
(free)
(free)
heap
heap
(free)
(free)
stack
stack
A 16-KB Address Space With 64-byte Pages
0000 0000
0000 0001
...
1111 1111
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
VPN
Offset

## Slide 19: A Detailed Multi-Level Example: Page Directory Idx
The page directory needs one entry per page of the page table
  it has 16 entries.
The page-directory entry is invalid  Raise an exception (The access is invalid)
14-bits Virtual address
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
VPN
Offset
Page Directory Index

## Slide 20: A Detailed Multi-Level Example: Page Table Idx
The PDE is valid, we have more work to do.
  To fetch the page table entry(PTE) from the page of the page table pointed to by this page-directory entry.
This page-table index can then be used to index into the page table itself.
14-bits Virtual address
13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
VPN
Offset
Page Directory Index
Page Table Index

## Slide 21: More than Two Level
In some cases, a deeper tree is possible.
30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Flag | Detail
Virtual address | 30 bit
Page size | 512 byte
VPN | 21 bit
Offset | 9 bit
offset
VPN

## Slide 22: More than Two Level : Page Table Index
In some cases, a deeper tree is possible.
30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
offset
Flag | Detail
Virtual address | 30 bit
Page size | 512 byte
VPN | 21 bit
Offset | 9 bit
Page entry per page | 128 PTEs
VPN
Page Table Index
Page Directory Index

## Slide 23: More than Two Level : Page Directory
If our page directory has entries, it spans not one page but 128.
To remedy this problem, we build a further level of the tree, by splitting the page directory itself into multiple pages of the page directory.
30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
offset
VPN
PD Index 0
PD Index 1
Page Table Index

## Slide 24: Multi-level Page Table Control Flow
01: VPN = (VirtualAddress & VPN_MASK) >> SHIFT
02: (Success,TlbEntry) = TLB_Lookup(VPN)
03: if(Success == True) //TLB Hit
04: if(CanAccess(TlbEntry.ProtectBits) == True)
05: Offset = VirtualAddress & OFFSET_MASK
06: PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
07: Register = AccessMemory(PhysAddr)
08: else RaiseException(PROTECTION_FAULT);
09: else // perform the full multi-level lookup
  (1 lines) extract the virtual page number(VPN)
  (2 lines) check if the TLB holds the transalation for this VPN
  (5-8 lines) extract the page frame number from the relevant TLB entry, and form the desired physical address and access memory

## Slide 25: Multi-level Page Table Control Flow
11: else
12: PDIndex = (VPN & PD_MASK) >> PD_SHIFT
13: PDEAddr = PDBR + (PDIndex * sizeof(PDE))
14: PDE = AccessMemory(PDEAddr)
15: if(PDE.Valid == False)
16: RaiseException(SEGMENTATION_FAULT)
17: else // PDE is Valid: now fetch PTE from PT
  (11 lines) extract the Page Directory Index(PDIndex)
  (13 lines) get Page Directory Entry(PDE)
  (15-17 lines) Check PDE valid flag. If valid flag is true, fetch Page Table entry from Page Table

## Slide 26: The Translation Process: Remember the TLB
18: PTIndex = (VPN & PT_MASK) >> PT_SHIFT
19: PTEAddr = (PDE.PFN << SHIFT) + (PTIndex * sizeof(PTE))
20: PTE = AccessMemory(PTEAddr)
21: if(PTE.Valid == False)
22: RaiseException(SEGMENTATION_FAULT)
23: else if(CanAccess(PTE.ProtectBits) == False)
24: RaiseException(PROTECTION_FAULT);
25: else
26: TLB_Insert(VPN, PTE.PFN , PTE.ProtectBits)
27: RetryInstruction()

## Slide 27: Inverted Page Tables
Keeping a single page table that has an entry for each physical page of the system.
The entry tells us which process is using this page, and which virtual page of that process maps to this physical page.